## Slide 1: Lab10
Presenter : LI YU XIANG

## Slide 2: Outline
use register as less as possible
gate all the registers
calculate before input has finished

## Slide 3: use register as less as possible
Registers not only consume power , but also take up space
In my IDC.v there are 6 registers :
Input counter(counter for current input)
Output counter(count for current output )
Operation counter(count for current processing operation)
Operation list(register that store the input operation)
Current pointer(point to current operation point in image)
Current state (FSM)

## Slide 4: The image that located at corner need less mux to decide the value, for example , the pixel at left up corner will be assigned only when operation pointer points to it.
Only be changed when operation pointer==0

## Slide 5: gate as more register as it can
The power can be lower if gate all the signal , but this will make JG take a huge time to complete , I am not sure about the reason, so I decide to gate the registers that store the input image.

## Slide 6: calculate before input has finish
Because the data can start to be calculated before input finish , so the cycles that need to wait after input finish can be reduce .
But some cases that need the value of last pixel still need to wait .

## Slide 7: thanks